## Slide 1: The RouteViews Project: Update
Patrick Okui
AfPIF 2025, Lagos
21 August 2025
Last updated 19th May 2025

## Slide 2: Background
RouteViews was first started in 1995
Now a growing network of 40+ collectors positioned strategically at Internet Exchange Points around the world
RouteViews collaborates with the Center for Applied Internet Data Analysis (CAIDA) working with NSF grants that support Designing a Global Measurement Infrastructure to Improve Internet Security, GMI3S (OAC-2131987), and an Integrated Library for Advancing Network Data Science, ILANDS (CNS-2120399).
RouteViews is supported with financial and in-kind donations by multiple organizations
RouteViews is based at the University of Oregon and operated by NSRC
NSRC supports the growth of global Internet infrastructure by providing engineering assistance, collaborative technical workshops, training, and other resources to university, research & education networks worldwide.
NSRC is partially funded by the IRNC program of the NSF (OAC-2029309) and Google with other contributions from public and private organizations.
The University of Oregon is a public research institution in Eugene, Oregon, USA founded in 1876.

## Slide 3: RouteViews Team Members
Hans Kuhn
Nina Bargisen
Owen Conway
Philip Smith
Philip Paeps
Anton Berezin

## Slide 4: What is RouteViews
A tool that allows Internet network operators to look at the BGP table from different backbones and locations around the world to troubleshoot and to assess:
  Reachability, hijacks, bugs, peer visibility, mass withdrawals, RPKI status,…
Operators who find it a valuable tool also peer to contribute to the value
RouteViews operates collectors strategically positioned at IXPs around the world.
  It also hosts a few multi-hop collectors at UO for those operators who are not present at IXPs.

## Slide 5: What is RouteViews
Many free and commercial tools used by network engineers every day include data from RouteViews
  CAIDA ASRANK
  CAIDA BGP Reader
  HE BGP Tools
  Kentik Market Intelligence
  Kentik BGP monitoring
  Catchpoint
  BGPMon
  And many more

## Slide 6: Make life easier for your NOC
route-views3.routeviews.org# sh ip bg 220.239.64.0
BGP routing table entry for 220.239.64.0/20, version 10370995
Paths: (1 available, best #1, table default)
Not advertised to any peer
38001 7473 4804 4804
202.150.221.33 from 202.150.221.33 (10.11.33.29)
Origin IGP, valid, external, best (First path received), rpki validation-state: invalid
Community: 38001:100 38001:3003 38001:8003
Last update: Sun Nov 10 14:28:09 2024
route-views3.routeviews.org#
RPKI state
upstream

## Slide 7: Make life easier for your NOC
route-views3.routeviews.org# sh ip bg 220.239.64.0/19
BGP routing table entry for 220.239.64.0/19, version 9454097
Paths: (25 available, best #24, table default)
Not advertised to any peer
9268 4764 1221 7474 4804, (aggregated by 4804 198.142.65.160)
203.62.187.103 from 203.62.187.103 (203.62.187.103)
Origin IGP, valid, external, atomic-aggregate, rpki validation-state: valid
Community: 0:2011 9268:2124
Last update: Mon Nov 4 04:04:03 2024
9268 4764 1221 7474 4804, (aggregated by 4804 198.142.65.160)
203.62.187.102 from 203.62.187.102 (203.62.187.102)
Origin IGP, valid, external, atomic-aggregate, rpki validation-state: valid
Community: 0:2011 9268:2124
Last update: Mon Nov 4 02:34:28 2024
route-views3.routeviews.org#
upstream

## Slide 8: RouteViews Impact
Barrett Lyon: https://www.youtube.com/watch?v=vo5glK9czIE

## Slide 9: Routeviews news
What’s happening at RouteViews

## Slide 10: RouteViews News
Collectors:
  All software collectors use FRR1 (version 10.2)
  One Cisco ASR1004 (as a tribute to the original!)
  Moving collectors from metal to VMs (easier deployment & management)
Location update:
  Most recent additions include GetaFIX (Philippines), KINX (Seol, Korea) and Namex (Italy)
  Several new locations offered; resources required to fulfil those offers
1FRRouting Project: https://frrouting.org/

## Slide 11: RouteViews Development Projects: API
API allows programmatic access to live RouteViews data
  (our collectors currently allow telnet access, which 1000s of automated scripts hammer daily)
Two access levels:
  Unauthenticated for casual (infrequent queries)
  Authenticated access (using verified PeeringDB users) for more serious research
API currently supports ten collectors
  More will be added as resources become available
Please consult the docs on how to use the API
  https://api.routeviews.org/docs/

## Slide 12: RouteViews Development Projects: LG
telnet access is unsustainable
  Gives open access to the collector command line interface to run “show” commands
Looking Glass will soon become the default access for each collector
  Permits the most commonly used BGP diagnostic commands
  telnet remains available on route-views.routeviews.org (the Cisco ASR1004) for legacy access
Looking Glass has completed internal testing and is now available for general use
  telnet access will be removed after due notice to the community

## Slide 14: RouteViews Development Projects: BMP
Live feed from collectors for BGP data consumers
Challenge is to make this scale and provide the infrastructure resources to support
stream being replaced by kafka cluster for better resilience
Notes: - we were using keepalived as the load balancer
- we were using openBMPD as the BMP collector

## Slide 15: RouteViews Behind the Scenes Projects
Upgrading archive infrastructure and storage
  RouteViews stores BGP data from 1997 – around 50 TBytes (compressed)
Tooling
  Automation tools for managing the whole infrastructure and deploying new peers
Collector OS (from CentOS to Ubuntu)
  CentOS end-of-life – half the collectors still running CentOS
FRR performance
  Tuning Linux TCP parameters to improve BGP peer performance
    https://fasterdata.es.net/host-tuning/linux/
  “Badly behaving peers” (aka slow and/or noisy peers)

## Slide 16: RouteViews Future Planning
Collectors & hosts in new locations outside North America
  Large IXPs with dense interconnection
  Unique or specialist environments (e.g. R&E exchanges)
Scalable and diverse archiving
Improved community support
  Running this infrastructure costs money!
  We hugely appreciate our generous supporters
    https://www.routeviews.org/routeviews/index.php/supporters/
Your recommendations are welcome! 🙏

## Slide 17: Consumers of RouteViews data
If you use RouteViews data for your products or services:
Please acknowledge the source!
  Your product or service likely would not work without our data!
Please do NOT send your customers of your products or services to us for technical support:
  We simply collect what is seen in the global routing table
  We cannot fix mistakes made by network operators
  We cannot fix bugs in BGP implementations
  We cannot remove BGP announcements we receive
  We cannot change what is seen in the global routing table

## Slide 18: Peering with routeviews
For Peering Coordinators

## Slide 19: Peering with RouteViews
RouteViews has a Selective peering policy
  PeeringDB: https://www.peeringdb.com/asn/6447
We require all peers to have a PeeringDB entry
  Our tools build peering options (for IXP based collectors) and configurations from PeeringDB
Peering:
  Over IPv4 (for IPv4 prefixes) and IPv6 (for IPv6 prefixes)
  We want to receive the entire BGP table (if operationally possible)
  We do not send you any prefixes (please don’t ask)

## Slide 20: RouteViews Peering Policy
General requirements:
Peer must operate stable equipment - RouteViews will shutdown BGP sessions that disturb the stability of the RouteViews platform
Peer must have a routable ASN
Peer must not be a hobby network
Peer’s full view of the global routing table is preferred
Routes should be aggregated as much as possible ( no longer than /24 for IPv4 and /48 for IPv6)
Peer must be present with up-to-date information in PeeringDB - including the NOC email address
Peer must filter RFC6890 space
RouteViews does not accept addpath-RX or TX
Peers must not send default routes
IXP peering:
We happily accept everyone's routes from the route servers.
We will set up bilateral sessions with anyone who meets the general requirements and will send us their full table.
We will peer at all mutual exchanges if requested.
Multihop peering:
We will accept multihop peers who are not on any mutual IXPs.
Peers must provide their full view of the Internet as they see it.
We accept two sessions for redundancy; more than two sessions can be set up if the feeds are sufficiently different.

## Slide 21: Why a Selective Peering policy?
Balancing operational overhead, scale and information from the data
Hobby Networks
Full View of the Internet
What makes a peering interesting?
  Networks in regions where we have limited visibility
  Networks demonstrating new interconnection patterns
  Networks using innovative routing practices
  Networks that help us understand emerging market dynamics
  Or maybe something we haven’t thought about yet

## Slide 22: Hosting routeviews
For potential hosts of collectors

## Slide 23: Hosting RouteViews
RouteViews is interested in new locations
  Especially in regions or economies we have no collector
  Where there are IXPs with large numbers of peers (>100)
Hosting a RouteViews collector
  Hosts can be IXPs themselves
  Hosts can be members of IXPs
  Hosts sponsor the IXP port and the (~10Mbps) transit required
  Hosts sponsor the VM needed for the collector
    Physical hardware is less preferred due to being harder to manage
    VMs sometimes may not be possible due to operational requirements

## Slide 24: Collector Specifications
Virtual Machine:
  16GB RAM min (prefer 32GB)
  100GB disk
  4 vCPUs
  1 transit interface (management and public CLI access, low traffic)
  1 peering interface on the IX
Physical Hardware:
  32GB – 64GB RAM
  400GB – 1TB SSD
  4+ CPUs
  Ethernet port for transit interface (1Gbps is enough)
  Ethernet port for IX peering (10Gbps is the standard now)

## Slide 25: Collector Software
Ubuntu 24.04 is RouteViews standard OS
  We require a minimal Ubuntu Server install
  Our deployment scripts do the rest
Routing daemon we install is FRR
  MRT1 used for BGP RIBs (archived every 2 hours) and BGP updates (archived every 15 minutes)
1 Multi-Threaded Routing Toolkit: https://datatracker.ietf.org/doc/html/rfc6396

## Slide 26: Collector Host
Acknowledged on RouteViews website as a sponsor
Contact details kept up to date with RouteViews team
  An up-to-date PeeringDB entry helps 😀

## Slide 27: SUPPORTING routeviews
How you can help

## Slide 28: Supporting RouteViews
The project was started in 1995 because network operators wished to see what their BGP announcements looked like from an external viewpoint
  Thousands of network operators & researchers all around the world now rely on RouteViews
  Many everyday tools we all rely on use RouteViews data
  Many commercial products and services rely on RouteViews data

## Slide 29: Supporting RouteViews
Please consider supporting RouteViews:
By peering with one of our collectors
By publicly acknowledging the value of the information we have collected
  For citations, our DOI is 10.7264/1y7v-2d90
If your product or service is commercially successful, we look forward to receiving your support to keep your product or service that way!
In any other way that helps keep this community service going

## Slide 30: RouteViews Collector Map
https://www.routeviews.org/routeviews/map/

## Slide 31: Thank you!